## Slide 1: A Monte Carlo Rendering Framework for Simulating Optical Heterodyne Detection
1 Juhyeon Kim 2 Craig Benko 2 Magnus Wrenninge 2 Ryusuke Villemin
2 Zeb Barber 1 Wojciech Jarosz 1 Adithya Pediredla
OHD Applications
Our Monte Carlo Simulator
FMCW Lidar
Blood Flow
Atmosphere
FMCW Lidar
Blood Flow
Atmosphere
Distance
Velocity
RGB
2
1
Project Page
Notes: Hi, today I will present our work titled a Monte Carlo rendering framework for simulating optical heterodyne detection

## Slide 2: Computational Imaging
Single Photon Imaging
Time-of-Flight Imaging
Polarization-based Imaging
Holographic Imaging
Interferometric Imaging
Speckle Imaging
Notes: I believe many of you in this room are engaged in the field of computational imaging. Over the past few decades, this field has advanced rapidly, leading to advances in techniques such as single-photon imaging, time-of-flight sensing, polarization imaging, speckle imaging, interferometry, and holography—several of which are featured in today’s talks.

## Slide 3: Rendering for Computational Imaging
Computational Imaging
Design a novel imaging hardware system
Build a better computational algorithms with enhanced capabilities
Replicate measurement of computational imaging systems through simulation
Exploit physically-accurate and efficient rendering algorithm
Digital Twin
Rendering for Computational Imaging
Notes: Like this, computational imaging typically aims to design novel hardware systems enhanced by advanced computational algorithms. However, the work I’ll be presenting today is slightly different from traditional computational imaging research. It is more closely aligned with rendering—what I call rendering for computational imaging. In this line of work, instead of building hardware, we build digital twins that closely replicate the imaging measurements using efficient and physically accurate rendering algorithms.

## Slide 4: Rendering for Computational Imaging
Transient / time-gated Rendering
[Jarabo et al. 2014]
[Pediredla et al. 2019]
Imaging System
Rendering
SPAD
Streak camera
Polarized imaging
Polarization Rendering
[Wilkie et al. 2012]
Speckle
Rendering
Speckle imaging
[Bar et al. 2019]
Doppler Rendering
?
Doppler Lidar / Blood / Wind Velocimetry
[Liu et al. 2022]
[Bar et al. 2020]
Notes: A well-known example would be rendering transient or time-gated sensors. Several techniques—such as kernel density estimation, ellipsoidal path connection, and temporally sliced photon primitives—have been proposed for this.
We also have well-established rendering theories for simulating polarized cameras, which are already integrated into renderers like Mitsuba. More recently, Monte Carlo frameworks for simulating speckle in far- and near-field have also been introduced. However, there is one important area that remained largely overlooked by rendering researchers until just a few years ago: Doppler imaging, for which no general-purpose scalable simulator exists.

## Slide 5: Doppler Effect
Notes: So, what is the Doppler effect? It is a phenomenon in which the frequency of a wave changes due to the relative motion between the source and the observer. A common example is the shift in pitch you hear from a moving sound source, like an ambulance.

## Slide 6: Intensity vs Field Doppler
Intensity
[Heide et al. 2015]
[Kim et al. 2023] (Also ours)
Doppler ToF (DToF) Imaging
Renderer
time (or distance)
What we see
Notes: In optical imaging systems, the Doppler effect manifests in two ways. The first is intensity Doppler, where the effect appears as a modulation in the intensity of the light source. Doppler Time-of-Flight imaging systems leverage this phenomenon, and two years ago, our group proposed an effective Monte Carlo simulator to model it.

## Slide 7: Intensity vs Field Doppler
Intensity
[Heide et al. 2015]
[Kim et al. 2023] (Also ours)
Doppler ToF (DToF) Imaging
Renderer
time (or distance)
What we see
Field Amplitude
Doppler Lidar
Blood Flow
This work
Optical Heterodyne Detection (OHD)
Wind
time (or distance)
Notes: The second is field Doppler, where the Doppler effect occurs in the electromagnetic field of the light itself. A well-known example is the red and blue shift observed in astronomy. However, this shift also occurs at smaller scales in applications such as Doppler lidar, blood or wind velocimetry. These techniques that rely on optical interference are collectively referred to as optical heterodyne detection. In this work, we present a scalable renderer for simulating such applications.

## Slide 8: Intensity vs Field Doppler Simulation
Intensity
time (or distance)
Field Amplitude
time (or distance)
Microscopic geometry relative to
Macroscopic
Microscopic
Explicit Move + Shift mapping
[Kim et al. 2023]
From Doppler Formula (Ours)
They measure different quantities and thus need different simulation!
(DToF)
(OHD)
Notes: So why do we need different renderers? These two types of Doppler effects fundamentally measure different physical quantities due to their large wavelength difference. Intensity Doppler captures macroscopic velocity, while Field Doppler detects microscopic velocity. As a result, we found that they require distinct simulation strategies. Actually, there are more interesting discussion on this comparison like shift mapping in rendering literature, but please refer to the paper for the details.

## Slide 9: Previous Works in OHD
[Jang et al., 2023]
[Nilsson et al., 1990]
[Bonner et al., 1981]
[Szczap et al., 2021]
[Hofrichter et al., 2024]
[Iiyama et al., 2017]
[Kim et al., 2020]
[Shafir et al., 2001]
Over-simplified, domain-specific assumptions
Notes: So going back to OHD simulation, there are several prior works that have explored OHD modeling or simulation, but they are limited in scope often relying on over-simplified, domain-specific assumptions.

## Slide 10: Our Monte Carlo Simulator
OHD Path Integral (Ours)
Path
Frequency
Radiometric
Path Throughput
Path
Path Integral [Veach 1997]
Radiometric
Path Throughput
Existing (Radiometric) Monte Carlo Path Tracers
Rendering for Computational Imaging
Standard Rendering
Notes: In contrast, our proposed algorithm—based on a path integral formulation that closely resembles the well-known expression from Veach in standard rendering—can leverage existing Monte Carlo path tracers, providing significant scalability across a wide range of OHD scenarios.

## Slide 11: Proposed Method

## Slide 12: OHD Principle
Object
Beam
Splitter
Reference Mirror
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Optical
Interference
Laser
Photodetector
Doppler shifted!
OHD Power Spectrum
FFT
Freq
Power
= 193.40001 THz
()
= 193.4 THz
0.00001 % different!
= 100MHz
Electronic device measurable
Beat frequency
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Notes: Let’s begin with the principle of OHD. A laser emits light at a frequency f_0, which is split by a beam splitter: one path reflects from a reference mirror, the other from the object. If the object is moving, the reflected light will have a Doppler-shifted frequency f. This shift is typically very small and is challenging to measure directly.
However, by interfering the reference and object beams, the photodetector produces measurements which oscillate at a frequency difference or beat frequency that is measurable by electronic devices.
By applying an FFT to the temporal measurements and finding the peak frequency, we compute the object’s velocity.

## Slide 13: OHD with Swept-Frequency Laser
Optical
Frequency
Doppler shift
Time-of-Flight
Reference
Received
Amplitude
Amplitude
Standard Laser
Swept-Freq
Laser
Optical
Frequency
Doppler shift
Reference
Received
FMCW lidar
(Frequency-Modulated Continuous-Wave)
Notes: Using a swept-frequency laser, we can measure not only object velocity from Doppler shift but also object distance, as the linearly varying frequency encodes both in the beat signal. FMCW lidar often uses triangular chirps to separate these two components.

## Slide 14: OHD Models
OHD system
Single object
Frequency
Power
Power
Frequency
is linear function of
No single beat frequency
OHD system
Non-line-of-sight (NLOS)
Glossy Object
Red Blood Cells
Aerosols
Notes: Many OHD applications adopt a simple single-bounce model, which produces a single peak depending on the object’s velocity and distance. However, this model fails in the presence of complex geometry and global illumination. Such scenarios typically occur in non-line-of-sight imaging, when scanning glossy surfaces, or dense particles such as red blood cells or aerosols.

## Slide 15: OHD Path Integral Formulation
(full derivation is in main paper)
OHD Path Integral
Power
: power spectrum density (PSD) of OHD
(magnitude square of the FFT result)
: path domain (all of the possible paths)
Freq
=
+
+
…
: radiometric
path throughput
Notes: To collectively address all of these scenarios, we derived a general and unified formulation for OHD measurements, which we call the OHD path integral.
The derivation includes many details, but the conclusion is very simple and intuitive. It evaluates the power spectral density of the OHD signal by accounting for all possible path contributions in the scene at all measurement frequencies. Importantly, f here is radiometric throughput—rather than complex field amplitudes—so we can leverage existing path tracers with minimal modifications to simulate OHD.

## Slide 16
Standard Rendering
Pixel output
Supports rich libraries!
Notes: Standard path tracer uses Monte Carlo method to synthesize an image like this, by accumulating the sampled path throughput at each pixel. Many renderers provide libraries that include various reflection and geometry models, as well as lots of efficient sampling techniques.

## Slide 17
Standard Rendering
Pixel output
OHD Rendering
Pixel output
① histogram
② Record
path velocity
path length
Can exploit all of the features in standard MC path tracers!
Frequency
Power
OHD Power Spectrum Density (PSD)
Notes: For OHD rendering, we still use existing path tracer but need to modify two things.
First, instead of single image, we output a sequence of image, or histogram at each pixel.
Second, for each sampled path, we also record path length and velocity at each path vertices.
Then, we build a histogram by accumulating path throughput to corresponding frequency bin, which is calculated from path length and path velocity which we recorded before.
And this eventually gives the PSD.
Again, we can make use of all of the features in existing standard path tracer also for OHD rendering!

## Slide 18
OHD Rendering
Transient Rendering
[Jarabo et al. 2014]
frequency
time
frequency
Power Spectrum
Transient Signal
time
Notes: In fact, OHD rendering is very similar to transient rendering that generates time-resolved image sequence or histogram at each pixel.
But unlike transient rendering which is resolved in time, OHD rendering is resolved in frequency domain as a power spectrum.

## Slide 19
OHD Rendering
Transient Rendering
[Jarabo et al. 2014]
frequency
time
Power Spectrum
Transient Signal
path velocity
path length
path length
Bin
Index
Notes: Also when determining bin index for sampled path, transient rendering uses only path length, while OHD rendering considers both path length and path velocity.

## Slide 20
Standard Rendering
Single
Value
OHD Rendering
Power
Spectrum
Transient Rendering
frequency
time
Transient Signal
Bin
Index
Pixel Output
Renderer Output
Path Integral
[Veach 1997]
[Jarabo et al. 2014]
[Ours]
Notes: Here is organized comparison between standard, transient and our proposed OHD rendering with governing path integrals.
Standard rendering outputs a single value, while transient and OHD both produce histogram, but in different manner.

## Slide 21: OHD Speckle Sampling
Measurement Index
Speckle
OHD Magnitude
Single Measurement (Accounts Speckle Effect)
Power Spectral Density
(Avg Power Spectrum)
Algorithm 1) Sample from Power Spectral Density
Freq
Freq
negative-exponential distribution
How to reproduce this?
Real Data Measurement
Algorithm 2) Add Random Phase to Each Path’s Optical Field
Time
Random Phase
Time
Time
+
+
Optical Field
Notes: Meanwhile, since OHD uses a coherent light source, its measurements are inherently affected by speckle noise when interacting with rough surfaces. To reproduce OHD speckle in our simulation, we propose two approaches: sampling from the previously evaluated PSD or directly calculating the optical field with added random phase.

## Slide 22: OHD Speckle Sampling
Frequency
Power (dB)
Single Measurement from Alg.2
Avg of 1000 Single Measurements
from Alg.1
With convolution
Both converges to same PSD!
Target Point
Notes: Both methods converge to the same result but differ in their appropriate use cases. For more details, please refer to the main paper.

## Slide 23: Applications of Our Simulators
Notes: Now, we demonstrate our simulation algorithm across three different OHD applications.

## Slide 24: Application (1) FMCW Lidar
Scan direction
Moving direction
Scan direction
Moving direction
Real data
Simulator
Retroreflector bars are used to indicate starting and end points!
Notes: First, for FMCW lidar, we compare our simulation with a real experiment in a scenario where a shiny copper surface is observed, with a treadmill moving behind it.

## Slide 25: Application (1) FMCW Lidar
Scan direction
Moving direction
treadmill
copper
ret
ret
ret
treadmill
copper
ret
ret
ret
Sample index along scan line
Sample index along scan line
Second
First
dominant hit point
Real data Reconstruction
Simulation Reconstruction
(A)
Real data
Simulator
Transition Region
Scan direction
Moving direction
distance (m)
velocity (m/s)
Slight calibration error exists!
PSD
PSD
Notes: We found that our simulator faithfully reproduces the real experiment in both distance and velocity reconstruction. One interesting observation is the presence of transition regions, where blurry reflection causes inaccurate reconstruction.
Our simulator is also capable to replicate these regions, with matching power spectrum.

## Slide 26: Application (2) Blood Flow Measurement
(A)
Real Data [Puyo18,19]
Simulation
Retinal Blood Flow Measurement
: Doppler
Images
Laser Doppler Velocimetry
Notes: Second, we simulate a non-invasive blood flow measurement scenario. Our simulator faithfully reproduces the results reported in a prior work on retinal blood flow measurement, capturing key features such as multi-bounce components in the Doppler spectrum.

## Slide 27: Application (2) Blood Flow Measurement
Real Data [Puyo18,19]
Simulation
Laser Doppler Velocimetry
: number of FFT windows
Notes: or OHD speckle patterns with respect to the number of FFT windows.

## Slide 28: Application (3) Wind Doppler Lidar
Aerosol
(1)
(2)
(3)
(4)
(1)
(2)
(3)
(4)
STFT
Time
Freq
ToF
Doppler
Shift
Coherent Wind Doppler Lidar
Real Data
[Wei21]
Simulation
Height (km)
0
1
Intensity
Freq
Freq
Freq
Multi-bounce only
Direct + Multi bounce
Notes: Finally, we simulate an atmospheric sensing scenario. Again, we find that our simulator closely matches results reported in prior work on wind and rainfall detection. Notably, our simulator also provides information that is not available in real-world—such as the decomposition of direct and multi-bounce components.

## Slide 29: Conclusion

## Slide 30: Conclusion : Comprehensive Doppler Simulator
[Kim et al. 2023] (Also ours)
This work
Intensity
Field Amplitude
Intensity
Doppler
Field
Doppler
Comprehensive Doppler Simulator
Notes: In conclusion, we propose a scalable Monte Carlo rendering algorithm for simulating optical heterodyne detection. Combined with our previous work on Intensity Doppler we now have a comprehensive simulation tool for modeling Doppler effects in computational imaging.

## Slide 31: Thank you!
Project Page : https://juhyeonkim95.github.io/project-pages/ohd_rendering/
OHD Applications
Our Monte Carlo Simulator
FMCW Lidar
Blood Flow
Atmosphere
FMCW Lidar
Blood Flow
Atmosphere
Distance
Velocity
RGB
Digital Twin
QR link :
Code, tutorials are available!
Implemented in Mitsuba!
Notes: Thank you for listening.
Please checkout the project page for code and tutorials.